Jünger Audio

Justus-von-Liebig-Str. 7

12489 Berlin

Germany

Tel:  +49 30 677721-0

Email: marc.judor@junger-audio.com

www.junger-audio.com

PRESS RELEASE

April 2009

Jünger Audio Introduces ESDI Cards AT NAB 2009

Berlin, Germany: Dynamics processing specialist Jünger Audio will be showing its range of new ESDI card at this year’s NAB Convention in Las Vegas.  Designed specifically for Satellite Digital Re Broadcasters, the ESDI card provides the ideal solution for controlling loudness for all incoming signals. Each SDI stream runs independently – the signals don’t need to be locked to a house reference.

The ESDI card combines one SDI interface with one DSP unit that automatically handles individual audio Loudness processing. It is designed for digital satellite TV, where SDI based incoming signals don’t match a uniform synchronisation and have widely varying levels. The basic version comes with an SD-SDI interface and offers 4-channels of LEVEL MAGIC processing. Upgrade to HD-SDI and to 8-channel Level Magic Surround are available by software license key.

Each ESDI card C8486 receives one TV channel through its SDI interface and then instantly processes that channel before re-transmitting it to the encoder. With ESDI in place, there is no need for synchronization and no change in the spectral range - just well controlled dynamics regardless the type or quality of the input.

Jünger Audio’s C8000 frames allow users to stack up to 16 different cards, thus providing 16 SDI channels. Thanks to the system’s embedded LEVEL MAGIC algorithm, users don’t need to worry about synchronising incoming sources before re-transmission or concern themselves with level issues because the system automatically handles the loudness control of all digital audio signals.

The dynamic range processor principles developed by Jünger Audio are based on a Multi-Loop dynamic range control principle in combination with adaptive controlled processing algorithms.

The LEVEL MAGIC Processor responsible for this Automatic Non Destructive Normalization process works with a Multi-Loop simultaneous combination of slow changes (AGC), fast changes (Transient Processing) and Look Ahead peak limiter management.

The unit is easy to operate as users only have to input a small number of settings when they begin using the system. Once these are in place, the system achieves optimum results by reviewing all other parameters necessary for inaudible processing and automatically controlling them in response to changes in the programme signal.

FEATURES:

• Combi SDI/DSP card – one card = one TV channel

• All parameters need only be set once via an easy to use web interface

• Includes LEVEL MAGIC adaptive controlled audio loudness processing (simultaneous AGC + Transient Processor for fast changes + Limiter)

• Fits into Jünger Audio’s C8000 Frames (up to 16 cards/16 TV channels per frame)

For more information about Jünger Audio’s ESDI card, please visit Jünger Audio at Booth N4937.

-ends-

About Jünger Audio

Established in Berlin in 1990, Jünger Audio specialises in the design and manufacture of high-quality digital audio dynamics processors. It has developed a unique range of digital processors that are designed to meet the demands of the professional audio market. All of its products are easy to operate and are developed and manufactured in-house, ensuring that the highest standards are maintained throughout. Its customers include many of the world’s top radio and TV broadcasters, IPTV providers, music recording studios and audio post production facilities.

# Text boxes

Press Contact

White Noise Public Relations

Tel/Fax: +44 (0) 1666 500142

Email: sue@whitenoisepr.co.uk