Jünger Audio

Justus-von-Liebig-Str. 7

12489 Berlin

Germany

Tel:  +49 30 677721-0

Email: marc.judor@junger-audio.com

www.junger-audio.com

PRESS RELEASE

June 2010

TV5’s Cable Viewers Reap The Benefits of Better Audio Thanks To Jünger Audio’s LEVEL MAGIC™ Technology

Berlin, Germany: Philippines-based television network Associated Broadcasting Company (TV5) has installed Jünger Audio’s LEVEL MAGIC™ technology to balance the audio transmissions it is sending to various cable operators throughout the country.

Currently owned by MediaQuest Holdings Inc., a subsidiary of Philippine Long Distance Telephone Company, TV5 has recently undergone a complete re-branding which has resulted in a substantially increased audience share. It now has more than 11% of the market, making it the third largest station in the Philippines.

TV5’s main facilities and transmitter are located in Quezon City, from where it delivers locally produced news, public affairs and entertainment programs throughout the country. The network is aiming to expand dramatically over the next year to cover more Filipino viewers, not only in the country but also the Filipino communities in the Middle East, United States and Europe.

Although most of TV5’s output goes through terrestrial transmission, the broadcaster also transmits through different cable operators in the country, with several relay stations in different major cities in the archipelago.

In order to level out these audio transmissions, TV5’s engineers specified a Jünger Audio C8000 LEVEL MAGIC™ system, which was supplied by Conversance Systems Network Solutions Inc., via Jünger Audio Asia. The system incorporates Jünger Audio’s adaptive loudness algorithm. This uses a Multi-Loop dynamic range control principle where slow changes (AGC), fast changes (Transient processing) and Look Ahead peak limiting are handled simultaneously, thus offering level management with exceptionally high audio quality and without coloration, pumping, breathing, distortion or modulation effects. The C8000 ensemble of frames, I/O interfaces and DSPs can be tailored to suit the different processing requirements of individual broadcasters. In TV5’s case the system incorporates an HD-SDI interface, which is specifically aimed at satellite, IPTV or cable re-broadcasters who are struggling with sync and loudness issues when re- broadcasting incoming signals.

Ed Castillo, Director of Engineering, says, “We have installed it in our Technical Operations Centre, after the playout server and before distribution. It has made a dramatic change to our audio output and its dynamic processing has really impressed our engineers because it gives such a quick response.”

Castillo adds that TV5 is so impressed with the results it has achieved with Jünger Audio’s LEVEL MAGIC technology that it plans to invest in more units in the future.

“LEVEL MAGIC has made a noticeable difference to our audio quality and we are looking forward to making this equipment part of the ongoing expansion and improvement of our system,” he says.

-ends-

About Jünger Audio

Established in Berlin in 1990, Jünger Audio specialises in the design and manufacture of high-quality digital audio dynamics processors. It has developed a unique range of digital processors that are designed to meet the demands of the professional audio market. All of its products are easy to operate and are developed and manufactured in-house, ensuring that the highest standards are maintained throughout. Its customers include many of the world’s top radio and TV broadcasters, IPTV providers, music recording studios and audio post production facilities.

# Text boxes

Press Contact

White Noise Public Relations

Tel/Fax: +44 (0) 1666 500142

Email: sue@whitenoisepr.co.uk